Yield: The Problem
data rate > retrieval rate
4800 b/s > 512 b/s

---
Yield: The Problem
Aggregate Network
Sampling Rate
Target Lifetime

---
Yield: The Problem
Aggregate Network Sampling Rate =
Reliable Transfer Rate
Aggregate Network
Sampling Rate
Bandwidth
Constrained
Full Signal
Collection
Target Lifetime

---
Yield: The Problem
Aggregate Network Sampling Rate *
Lifetime Target * Joules / Byte = Battery Capacity
Aggregate Network
Sampling Rate
Full Signal
Collection
Energy
Constrained
Target Lifetime

---
Yield: The Problem
Energy and
Bandwidth
Constrained
Aggregate Network
Sampling Rate
Bandwidth
Constrained
Full Signal
Collection
Energy
Constrained
Target Lifetime

---
Data Has Value
100Hz Seismometer, Volcan Reventador 2005
Small
Earthquake
Noise
interesting data
Large
Eruption
Large
Eruptions
Large
Eruption
Large
Eruptions

---
Assigning Value
Summaries should be small (relative to ADU size) and easy to compute
Signal Bandwidth: 18000 B/min
Summary Bandwidth: 4 B/min
Volcano Application Example: RSAM
Raw signal
Reduced
Seismic
Amplitude
Measurement
(RSAM)
[Speaker Notes: Used by seismic community, more interesting data, etc.]

---
Data Has Cost
7
6
2
5
4
1
3
B
Bandwidth to Node 1:
1024 Bytes/sec
Bandwidth to Node 7:
512 Bytes/sec
(Bandwidth for reliable data transfer)

---
Assigning Cost
Empirically measure:
id: energy consumption during downloading
ir: energy consumption during routing
io: energy consumption during overhearing
Multiply by estimated transfer time to get power
B
3
4
5
6
7
1
2

---
Assigning Cost
Empirically measure:
id: the current draw during downloading
ir: the current draw during routing
io: the current draw during overhearing
Multiply by estimated transfer time to get power
B
3
4
5
6
7
1
2
B
3
4
5
6
7
1
2

---
Assigning Cost
Empirically measure:
id: the current draw during downloading
ir: the current draw during routing
io: the current draw during overhearing
Multiply by estimated transfer time to get power
 c7 = (0, 0, ir, io, ir, io, id) * t7
B
3
4
5
6
7
1
2
B
3
4
5
6
7
1
2
B
3
4
5
6
7
1
2

---
Cost Vectors
Energy cost expressed as a vector c
ci = energy needed to download ADU on Node i
(Initial cost vector estimated based on download history and knowledge of the transfer protocol)

---
Lance
Given extraction cost and data value:
Maximize total value retrieved, subject to bandwidth and energy constraints

---
Lance Architecture

---
Lance Architecture
1) Nodes sample data to ADUs

---
Lance Architecture
2) Nodes compute summary for each ADU

---
Lance Architecture
2) Nodes compute summary for each ADU
3) Summaries sent to base station

---
Lance Architecture
4) ADUs logged to Flash

---
Lance Architecture
On the Base Station
(1)
Assign Value,Cost
1) Initial Value, Cost Computed
2) Value Modified by Policy Modules
3) ADUs Scored by Lance Optimizer
4) Top-Scoring ADU Downloaded
Policy Modules
Optimizer
Download
[Speaker Notes: Replace with flowchart]

---
Lance Architecture
On the Base Station
(2)
(1)
Assign Value,Cost
1) Initial Utility, Cost Computed
2) Value Modified by Policy Modules
3) ADUs Scored by Lance Optimizer
4) Top-Scoring ADU Downloaded
Policy Modules
Optimizer
Download

---
Lance Architecture
On the Base Station
(2)
(3)
(1)
Assign Value,Cost
1) Initial Value, Cost Computed
2) Values Modified by Policy Modules
3) ADUs Scored by Lance Optimizer
4) Top-Scoring ADU Downloaded
Policy Modules
Optimizer
Download

---
Lance Architecture
On the Base Station
(2)
(3)
(1)
(4)
Assign Value,Cost
1) Initial Value, Cost Computed
2) Values Modified by Policy Modules
3) ADUs Scored by Lance Optimizer
4) Top-Scoring ADU Downloaded
Policy Modules
Optimizer
Download

---
Optimization Goal
U = all possible ADUs
B = initial node battery state constraint vector
c(u), v(u) are the cost, value of an ADU (or set of ADUs)
The optimal set uo is the set of ADUs maximizing
∑ v(uo) subject to ∑ c(uo) < B

---
Optimization Goal
U = all possible ADUs
B = initial node battery state constraint vector
c(u), v(u) are the cost, value of an ADU (or set of ADUs)
The optimal set uo is the set of ADUs maximizing
∑ v(uo) subject to ∑ c(uo) < B
Offline Solution: Multidimensional Knapsack Problem
c(u) are weights,
v(u) are values,
Bi's are knapsack capacities
Used to produce optimality bound

---
Optimization Strategy
Goal: Online Approximation of Offline Optimal
1) Examine all available ADUs
2) Assign each a score via scoring function
3) Download top-scoring ADU if resources available

---
Scoring Functions
Inputs: ADU with value, cost vector
Output: Score used to rank ADUs
Use the most significant component of the cost to weight the value of the ADU
s = v
1) Value Only
s = v over { sum c_i }
2) Cost Total
s = v over c_j newline c_j over B_j > c_i over B_i forall i neq j
3) Cost Bottleneck

---
Scoring Functions
Simulation Results:
10-node linear topology
Biased towards nodes near sink
Same from all nodes
Almost matches
optimal

---
2007 Deployment
1 Week deployment
Volcan Tungarahua
August 2007
8 nodes
Seismic and acoustic sensors

---
2007 Deployment

---
Deployment Evaluation
Lance extracted 99.5% of the
offline optimal value

---
Backup Slides Follow
challen@eecs.harvard.edu
http://www.eecs.harvard.edu/~challen/

---
Lance: Mercury