Limitations to Lance
1) Centralized solution: doesn't scale to larger networks
2) Limited to data collection: can't control other components that consume energy

---
In a Perfect World...
7
6
2
5
4
1
One, Big, Battery:
Shared by all nodes
Infinite capacity
3
B

---
In a Perfect World...
7
6
5
4
One, Big, Battery:
Shared by all nodes
Infinite capacity
:: Load distribution does not matter
:: All charge captured is stored
:: No node must go offline until entire battery is exhausted
B

---
In Our World...
7
6
5
4
Many, Small, Batteries:
Local at each node
Finite capacity
:: Load distribution matters.
:: Captured charge can be wasted.
:: Nodes will go offline while energy available at other nodes.
B

---
Improving Load Distribution
Goal: Improve application fidelity by matching system load to availability
:: Capture all incident energy
:: Shift load towards underutilized nodes
:: Shift load away from threatened nodes

---
Improving Load Distribution
Goal: Improve application fidelity by matching system load to availability
:: Capture all incident energy
:: Shift load towards underutilized nodes
:: Shift load away from threatened nodes
Cannot perform all actions in the way that minimizes the total energy consumed by all involved nodes!

---
Routing Problem
Assuming Nodes 1, 2 and 3 are routing data at fixed rates to the base station Node 0:
?
represents the amount of energy (in mJ) necessary to successfully transmit a packet across the link.
0
0.5
0.5
1.0
1.0

---
Routing Problem
Assuming the application needs inputs from all three nodes, the the network lifetime is equal to the time that the first node goes offline!
Assuming Nodes 1, 2 and 3 are routing data at fixed rates to the base station Node 0:
?
0
0.5
0.5
1.0
1.0

---
Routing Problem
Assuming Nodes 1, 2 and 3 are routing data at fixed rates to the base station Node 0:
Note that the route 3,1,0 consumes the least energy for Node 3...
0
0.5
0.5
1.0
1.0

---
Routing Problem
Assuming Nodes 1, 2 and 3 are routing data at fixed rates to the base station Node 0:
Note that the route 3,1,0 consumes the least energy for Node 3...
Note that the route 3,1,0 consumes the least energy for Node 3... and the least energy overall!
0
0.5
0.5
1.0
1.0

---
Routing Problem
Assuming Nodes 1, 2 and 3 are routing data at fixed rates to the base station Node 0:
When is route 3,1,0 actually the wrong choice?
(Or when does route 3,2,0 lead to a better network outcome?)
Note that the route 3,1,0 consumes the least energy for Node 3...
Note that the route 3,1,0 consumes the least energy for Node 3... and the least energy overall!
0
0.5
0.5
1.0
1.0

---
Routing Problem
Assuming Nodes 1, 2 and 3 are routing data at fixed rates to the base station Node 0:
When is route 3,1,0 actually the wrong choice?
(Or when does route 3,2,0 lead to a better network outcome?)
Four Cases:
1) Differences in availability
0
?
Node	Energy
1	10
2	30
3	25
(Assume Sink 0 is powered)
0.5
0.5
1.0
1.0

---
Routing Problem
Assuming Nodes 1, 2 and 3 are routing data at fixed rates to the base station Node 0:
When is route 3,1,0 actually the wrong choice?
(Or when does route 3,2,0 lead to a better network outcome?)
Four Cases:
1) Differences in availability
:: Using Route 3,1,0:
0
Node	Energy
1	10
2	30
3	25
T=0
(Assume Sink 0 is powered)
0.5
0.5
1.0

---
Routing Problem
Assuming Nodes 1, 2 and 3 are routing data at fixed rates to the base station Node 0:
When is route 3,1,0 actually the wrong choice?
(Or when does route 3,2,0 lead to a better network outcome?)
Four Cases:
1) Differences in availability
:: Using Route 3,1,0:
Lifetime = 10, 40 units left
0
Node	Energy
1	0
2	20
3	20
T=10
(Assume Sink 0 is powered)
0.5
0.5
1.0

---
Routing Problem
Assuming Nodes 1, 2 and 3 are routing data at fixed rates to the base station Node 0:
When is route 3,1,0 actually the wrong choice?
(Or when does route 3,2,0 lead to a better network outcome?)
Four Cases:
1) Differences in availability
:: Using Route 3,1,0:
Lifetime = 10, 40 units trapped
:: Using Route 3,2,0:
0
Node	Energy
1	10
2	30
3	25
T=0
(Assume Sink 0 is powered)
0.5
1.0
1.0

---
Routing Problem
Assuming Nodes 1, 2 and 3 are routing data at fixed rates to the base station Node 0:
When is route 3,1,0 actually the wrong choice?
(Or when does route 3,2,0 lead to a better network outcome?)
Four Cases:
1) Differences in availability
:: Using Route 3,1,0:
Lifetime = 10, 40 units trapped
:: Using Route 3,2,0:
Lifetime = 15, 12.5 units trapped
0
Node	Energy
1	2.5
2	0
3	10
T=15
(Assume Sink 0 is powered)
0.5
1.0
1.0

---
Routing Problem
Assuming Nodes 1, 2 and 3 are routing data at fixed rates to the base station Node 0:
When is route 3,1,0 actually the wrong choice?
(Or when does route 3,2,0 lead to a better network outcome?)
Four Cases:
1) Differences in availability
2) Differences in non-routing load
0
?
0.5
0.5
1.0
1.0

---
Routing Problem
Assuming Nodes 1, 2 and 3 are routing data at fixed rates to the base station Node 0:
When is route 3,1,0 actually the wrong choice?
(Or when does route 3,2,0 lead to a better network outcome?)
Four Cases:
1) Differences in availability
2) Differences in non-routing load
3) Differences in charging rates
0
?
0.5
0.5
1.0
1.0

---
Routing Problem
Assuming Nodes 1, 2 and 3 are routing data at fixed rates to the base station Node 0:
When is route 3,1,0 actually the wrong choice?
(Or when does route 3,2,0 lead to a better network outcome?)
Four Cases:
1) Differences in availability
2) Differences in non-routing load
3) Differences in charging rates
4) Overcharging
0
?
0.5
0.5
1.0
1.0

---
Our Idea
Integrated
Distributed
Energy
Awareness

---
Awareness

---
Awareness
O(L, B, C) = min(Bi / Li)

---
Awareness
O(L, B, C) = min(Bi / Li)
s = (Null, Node 0, Node 0, Node 1)
L = (0, 1.0, 1.0, 0.5)
B = (∞, 10, 30, 25); C = (0, 0, 0, 0)
0
0.5
0.5
1.0

---
Awareness
O(L, B, C) = min(Bi / Li)
s = (Null, Node 0, Node 0, Node 1)
L = (0, 1.0, 1.0, 0.5)
B = (∞, 10, 30, 25); C = (0, 0, 0, 0)
O(L, B, C) = 10
0
0.5
0.5
1.0

---
Awareness
O(L, B, C) = min(Bi / Li)
s = (Null, Node 0, Node 0, Node 1)
L = (0, 1.0, 1.0, 0.5)
B = (∞, 10, 30, 25); C = (0, 0, 0, 0)
O(L, B, C) = 10
0
s = (Null, Node 0, Node 0, Node 2)
L = (0, 0.5, 2.0, 1.0)
B = (∞, 10, 30, 25); C = (0, 0, 0, 0)
0
0.5
0.5
1.0
0.5
1.0
1.0

---
Awareness
O(L, B, C) = min(Bi / Li)
s = (Null, Node 0, Node 0, Node 1)
L = (0, 1.0, 1.0, 0.5)
B = (∞, 10, 30, 25); C = (0, 0, 0, 0)
O(L, B, C) = 10
0
s = (Null, Node 0, Node 0, Node 2)
L = (0, 0.5, 2.0, 1.0)
B = (∞, 10, 30, 25); C = (0, 0, 0, 0)
O(L, B, C) = 15
0
0.5
0.5
1.0
0.5
1.0
1.0

---
Awareness: Global State
IDEA Optimizer
O(L(S), B, C)
Energy
Objective
Function
Global State
Not known at any node
Most state changes affect only local neighbors
Perform local optimization using local information
Does not guarantee global optimality!

---
Our Idea
Integrated
Distributed
Energy
Awareness

---
Distribution
What does Node 3 need to know?
0
?
0.5
0.5
1.0
1.0

---
Distribution
0
?
B = (??, ??, ???, 25)
C = (??, ??, ??, 0)
L1 = (??, 0.5, ??, 0.5)
L2 = (??, ??, 1.0, 1.0)
0.5
0.5
1.0
1.0

---
Distribution
0
?
B = (??, ??, ???, 25)
C = (??, ??, ??, 0)
L1 = (??, 0.5, ??, 0.5), E(L1,B,C) = 50
L2 = (??, ??, 1.0, 1.0), E(L2,B,C) = 25
0.5
0.5
1.0
1.0

---
Distribution
0
B = (??, ??, ???, 25)
C = (??, ??, ??, 0)
L1 = (??, 0.5, ??, 0.5), E(L1,B,C) = 50
L2 = (??, ??, 1.0, 1.0), E(L2,B,C) = 25
0.5
0.5
1.0

---
Distribution
0
?
B = (??, ??, ???, 25)
C = (??, ??, ??, 0)
L1 = (??, 0.5, ??, 0.5), E(L1,B,C) = 50
L2 = (??, ??, 1.0, 1.0), E(L2,B,C) = 25
L = 0.5
B = 10
C = 0
0.5
0.5
1.0
1.0

---
Distribution
L = 0.5
B = 10
C = 0
0
?
B = (??, 10, ???, 25)
C = (??, 0, ??, 0)
L1 = (??, 1.0, ??, 0.5), E(L1,B,C) = 10
L2 = (??, 0.5, 1.0, 1.0), E(L2,B,C) = 20
0.5
0.5
1.0
1.0

---
Distribution
0
?
B = (??, 10, ???, 25)
C = (??, 0, ??, 0)
L1 = (??, 1.0, ??, 0.5), E(L1,B,C) = 10
L2 = (??, 0.5, 1.0, 1.0), E(L2,B,C) = 20
L = 1.0
B = 30
C = 0
0.5
0.5
1.0
1.0

---
Distribution
0
?
B = (??, 10, 30, 25)
C = (??, 0, 0, 0)
L1 = (??, 1.0, 1.0, 0.5), E(L1,B,C) = 10
L2 = (??, 0.5, 2.0, 1.0), E(L2,B,C) = 15
L = 1.0
B = 30
C = 0
0.5
0.5
1.0
1.0

---
Distribution
0
1.0
B = (??, 10, 30, 25)
C = (??, 0, 0, 0)
L1 = (??, 1.0, 1.0, 0.5), E(L1,B,C) = 10
L2 = (??, 0.5, 2.0, 1.0), E(L2,B,C) = 15
0.5
1.0

---
Distribution: Overhead
Data
Sharing
IDEA Optimizer
O(L(S), B, C)
Shared Data
(C0, B0, L0)
. . .
Energy
Objective
Function
(Cn, Bn, Ln)
Load
Model
Battery
Monitor
Charge
Model
Distribution Overhead:
Can be significant
Most changes affect only local neighbors
Distribute state locally or only over k hops
Charge
Monitor
Load
Monitor

---
Our Idea
Integrated
Distributed
Energy
Awareness

---
Integration
App
State
State 1
(s10,s11,s12...)
App
O(L, B, C) ∙ α + u(s) ∙ (1 - α)
State 2
(s20,s21,s22...)
State 3
(s30,s31,s32...)
Example Applications:
Routing Layers
MAC Protocols
Distributed Consensus	Algorithms
Distributed Computation

---
Integration
App
State
State 1
(s10,s11,s12...)
App
O(L, B, C) ∙ α + u(s) ∙ (1 - α)
State 2
(s20,s21,s22...)
State 3
(s30,s31,s32...)
Example Applications:
Routing Layers
MAC Protocols
Distributed Consensus	Algorithms
Distributed Computation

---
Integration
App
State
State 1
(s10,s11,s12...)
App
O(L, B, C) ∙ α + u(s) ∙ (1 - α)
State 2
(s20,s21,s22...)
State 3
(s30,s31,s32...)
α is the energy weighting factor
α = 1 → optimize only for energy
α = 0 → optimize only for application utility
(O() and u() must be normalized to between 0 and 1)
Example Applications:
Routing Layers
MAC Protocols
Distributed Consensus	Algorithms
Distributed Computation

---
ICTP Results
Charging Nodes

---
ICTP Results
Charging Nodes

---
ICTP Results

---
Backup Slides Follow
challen@eecs.harvard.edu
http://www.eecs.harvard.edu/~challen/

---
Effects of Load Distribution
One, Big, Battery Optimal System
Incident
Charge

---
Effects of Load Distribution
One, Big, Battery Optimal System
100% captured and devoted to maximizing application fidelity
Incident
Charge

---
Effects of Load Distribution
One, Big, Battery Optimal System
100% captured and devoted to maximizing application fidelity
Incident
Charge
All actions performed in the way that minimizes the total energy consumed by all involved nodes.

---
Effects of Load Distribution
Non-Distribution Aware System
Incident
Charge

---
Effects of Load Distribution
Non-Distribution Aware System
Wasted charging full batteries
Incident
Charge

---
Effects of Load Distribution
Non-Distribution Aware System
Wasted charging full batteries
Trapped at nodes unable to improve application fidelity
Incident
Charge

---
Effects of Load Distribution
Non-Distribution Aware System
Wasted charging full batteries
Trapped at nodes unable to improve application fidelity
Incident
Charge
Devoted to maximizing application fidelity

---
Improving Load Distribution
Distribution Aware System
Wasted charging full batteries
Trapped at nodes unable to improve application fidelity
Incident
Charge
Devoted to maximizing application fidelity

---
Improving Load Distribution
Distribution Aware System
Wasted charging full batteries
Trapped at nodes unable to improve application fidelity
Incident
Charge
Devoted to maximizing application fidelity

---
Improving Load Distribution
Distribution Aware System
Wasted charging full batteries
Trapped at nodes unable to improve application fidelity
Incident
Charge
Devoted to maximizing application fidelity

---
Improving Load Distribution
Distribution Aware System
Wasted charging full batteries
Trapped at nodes unable to improve application fidelity
Overhead of distributing energy information
Incident
Charge
Devoted to maximizing application fidelity

---
Improving Load Distribution
Distribution Aware System
Wasted charging full batteries
Trapped at nodes unable to improve application fidelity
Overhead of distributing energy information
Improvement in application fidelity
Incident
Charge
Devoted to maximizing application fidelity